## Slide 1: Fractional factorial designs

## Slide 2: Fractional factorial design
2k-p：k factors with 2 levels each, (1/2)p Fraction
  26-1: 6 factors with 2 levels each, 1/2 Fraction
  28-2: 8 factors with 2 levels each, 1/4 Fraction
  R: resolution
元智大學 江行全教授

## Slide 3: DEVELOPING A TWO-LEVEL FRACTIONAL FACTORIAL
A Full Factorial Experiment
Cell A B AB C AC BC ABC
(1) - - + - + + -
a + - - - - + +
b - + - - + - +
ab + + + - - - -
c - - + + - - +
ac + - - + + - -
bc - + - + - + -
abc + + + + + + +

## Slide 4: Starting the Plan for A Fractional Factorial Experiment
Cell A B D C AC BC ABC
(1) - - + - + + -
a + - - - - + +
b - + - - + - +
ab + + + - - - -
c - - + + - - +
ac + - - + + - -
bc - + - + - + -
abc + + + + + + +
AB
Alias

## Slide 5: Algebra of Signs
Axioms
  anything squared is a (+)
  A (+) times anything changes nothing
Example
  sign D = sign AB
  Thus, in sign algebra D = AB
  To find the alias for A, eliminate B
  Multiply both sides by the sign of B
  And + changes nothing by Axiom # 2
  BD = A
  An alias of A is the BD interaction
  (the sign of BD will always match
  the sign of A)
Cell A B D C AC BC ABC
(1) - - + - + + -
a + - - - - + +
b - + - - + - +
ab + + + - - - -
c - - + + - - +
ac + - - + + - -
bc - + - + - + -
abc + + + + + + +
AB
Alias

## Slide 6: A Fractional Factorial Experiment
Cell A B D C AC BC ABC
(1) - - + - + + -
a + - - - - + +
b - + - - + - +
ab + + + - - - -
c - - + + - - +
ac + - - + + - -
bc - + - + - + -
abc + + + + + + +
Alias BD AD AB ABCD BCD ACD CD
I=ABD ∴ABD is lost and gone forever

## Slide 7: Aliases and the Principal Generator
Generator equation: I=ABD
Factors | Aliases
A | A=A2BD=BD
B | B=AB2D=AD
AB | AB=A2B2D=D
C | C=ABCD
AC | AC=A2BCD=BCD
BC | BC=AB2CD=ACD
ABC | ABC=A2B2CD=CD

## Slide 8: 4 Variables, at 2 Levels
Test combination = Ln = 24 = 16
Number of contrasts = Ln –1 = 15
24-1 (same size as a 23)
Contrasts 7
Aliases 7
Identities 1
------------------------------------------
Total 15

## Slide 9: A Fractional Factorial Experiment
Cell A B D C E BC ABC
(1) - - + - + + -
a + - - - - + +
b - + - - + - +
ab + + + - - - -
c - - + + - - +
ac + - - + + - -
bc - + - + - + -
abc + + + + + + +
Identities and Aliases
Alias
AB
AC

## Slide 10: Aliases and the Generators
I1=ABD I2=ACE I3=ABDxACE=BCDE |  |  | 
A | BD | CE | ABCED
B | AD | ABCE | CDE
D | AB | ACED | BCE
C | ABCD | AE | BDE
E | ABDE | AC | BCD
BC | ACD | ABE | DE
ABC | CD | BE | ADE

## Slide 11: A Fractional Factorial Experiment
Cell A B D C E BC ABC
(1) - - + - + + -
a + - - - - + +
b - + - - + - +
ab + + + - - - -
c - - + + - - +
ac + - - + + - -
bc - + - + - + -
abc + + + + + + +
Alias
BD AD AB ABCD ABDE ACD CD
CE ABCE ACED AE AC ABE BE
ABCDE CDE BCE BDE BCD DE ADE

## Slide 12: A Fractional Factorial Experiment
Factors: A, B, C, D and E
Contrasts: 25-1=32-1=31
25-2(same size as a 23)
Contrasts 7
Aliases 21
Identities (lost) 3
--------------------------------------
Total 31

## Slide 13: Defining Relation and Generating Functions
27-3 Fractional Factorial (1/8 fraction)
Principal Generators: E = ABC, F = BCD, G = ABD
Defining Relation:
I = ABCE = BCDF = ABDG = ADEF
= CDEG = ACFG = BEFG

## Slide 14: Defining Relation
A relationship used to show the confounded sets of factors in a fractional design
For example: I = ABCD
Effect | Alias
A | BCD
B | ACD
C | ABD
D | ABC
AB | CD
AC | BD
AD | BC
BC | AD
BD | AC
CD | AB
ABC | D
ABD | C
ACD | B
BCD | A
ABCD | I

## Slide 15: Definition of Resolution
The length of the shortest word in the defining relation of a two-level design
Resolution V(R V) (unsaturated design)
  Unconfounded main effects and 2-way Interactions
  For example: 25-1,I=ABCDE
  Resolution IV (R IV) (unsaturated design)
  Unconfounded main effects, but 2-way interactions are confounded with other 2-way interactions
  For example: 24-1,I=ABCD
Resolution III (R III) (Saturated design)
  Main effects are confounded with 2-way interactions
  For example: 23-1,I=ABC
Resolution II (R II) (Supersaturated design)
  Main effects are confounded with other main effects
  For example: 22-1,I=AB

## Slide 16: Minimum Confounding
Only the 4 factor interaction is lost. Main effects and two factor Interactions can be separated by running another experiment
Cell A B AB C AC BC D
(1) - - + - + + -
a + - - - - + +
b - + - - + - +
ab + + + - - - -
c - - + + - - +
ac + - - + + - -
bc - + - + - + -
abc + + + + + + +
Alias
BCD ACD CD ABD BD AD ABC
I = ABCD ABCD is lost and gone forever

## Slide 17: Fractional Factorial Experiment Design
Basically, the strategic arrangement for Fractional Factorial Experiment Design can be divided into the following three stages
Stage 1
(Preparation and Design Selection) Select k input variables/factors and two (high and low) levels which are anticipated to have an effect on the responses. select responses/output variables.

## Slide 18: Fractional Factorial Experiment Design
Stage 2
(Execution and Data analysis) Conduct experiment run, collect and record the data Perform Yates’s Algorithm and/or Analysis of Variance to estimate the effects of input variables and determine the significant effects using normal probability plot.
Stage 3
(Prediction and Confirmation) Develop a fitted model for the responses. Draw conclusions and make predictions. Perform confirmatory tests. Assess the results and make decisions/recommendations.

## Slide 19: Planning For DOE
241=16
232=16
224=16
y>1
y=1
322=18
331=27
L36(23313
L27 (312)
L9(34)
L18 (21.37)
4k7
k3
l=3
5k8
l=2
L8(27)
L12(211)
L16(215)
Numb.ofKey Charact.
k=5
k=6
25-1
26-2
k=7
k=8
27-4
28-4
解
析
度
(IV)
(Ⅲ)
一、Selection between lk (full), lk-p (fractional), Taguchi

## Slide 20: Planning For DOE (Cont’)
二、Data Analysis Procedure
Perform Effect Normal Probability Plot
Perform Effect Pareto Plot
Conduct ANOVA to confirm the key factors
Establish Prediction/Regression Equation
Perform residual analysis (Normal probability plot) and Lack of Fit test for fitted Model/ Regression Equation
Perform confirmatory test (MAPE<5%)

## Slide 21: Class Exercise
Five factors in a manufacturing process for an integrated circuit were investigated in a 25-1 design with the objective of improving the process yield.
  A：aperture setting (small, large)
  B：exposure time (20% below or above nominal)
  C：develop time (30, 45 sec)
  D：mask dimension (small, large)
  E：etch time (14.5, 15.5 min)
資料來源 Montgomery 5th ed., p.311

## Slide 22: Class Exercise
使用Minitab來建構、分析及解釋部分因子實驗(fractional factorial experiment)
There are 5 factors and 1 response (process yield)
Use Minitab to establish a fractional factorial experiment
Only 16 experiments can be conducted in this ffe.
 | -1 level | +1 level
X1= aperture setting | small | large
X2= exposure time | below 20% | above 20%
X3= develop time | 30 | 45
X4= mask dimension | small | large
X5= etch time | 14.5 | 15.5
資料來源 Montgomery 5th ed., p.311

## Slide 23: Pareto Chart of Standardized Effects
The factos A, B, C and AB are significant (important)

## Slide 24: Normal Probability Plot
30
20
10
0
1
0
-1
Effect
N
o
r
m
a
l
S
c
o
r
e
AB
C
A
B
Normal Probability Plot of the Effects
(response is yield, Alpha = .10)
A:
aperture
B:
exposure
C:
develop
D:
mask dim
E:
etch

## Slide 25: ANOVA Table for Best Model
All variables statistically significant, p value less than 0.1
Lack of fit >0.05
表示目前模式是適合的
Yield=30.313+5.562*aperture setting+16.937*exposure time
+5.437*develop time+3.438*aperture setting *exposure time

## Slide 26: Practical Significant of Results
We need to run General Linear Model to determine the practical significant of the terms we are interested in
Tip: change the display into coded units first
Stat  ANOVA  General Linear Model
迴歸模式中的因子

## Slide 27: General Linear Model: ANOVA
% contribution is just the proportion of the total
SS for each variable and interaction (source)
Source | SS | % contribution
aperture setting | 495.1 | 8.57
exposure time | 4590.1 | 79.48
develop time | 473.1 | 8.19
aperture * exposure | 189.1 | 3.27
Error | 28.2 | 
Total | 5775.4 | 
Highest contribution