## Slide 1: Evaluation GR&R for the weight of Golf Ball
Reporter : | 
Pei-Jen, Tsai | R26991062
Tse-Wei, Su | R26001134
Lin Chao | RA7001070
Instructor : | Prof. Jeh-Nan Pan

## Slide 2: Outline
Introduction
Goal of Study
Sample Collection
Data Analysis
Conclusion

## Slide 3: Introduction
Driving for show and Putt for money
Driving distance of golf ball bases on two factors:
1.Speed of swing.
2.The structure of golf ball
a. Weight : No more than 45.93 gm
b. Diameter : No less than 42.67 mm
c. Dimples : Numbering from 250 to 450

## Slide 4: Goal of Study
Evaluating GR&R for weight of golf balls to estimate the accuracy and precision of the measure methods and the variation of golf balls.
Moving from learning to doing.
The “longer distance” advertisement abides by the regulation.

## Slide 5: Systematic Problem Solving Flowcharts
Start
Obtain 20 samples.
The weight of each golf ball was measured by using the digital scale.
Each golf ball was measured twice by each operator.
The measurement results were recorded in Minitab software.
The data was analyzed using control charts, classical GRR and ANOVA
Conclusions were formulated according to the objectives of the experiment
End

## Slide 6: Cause and Effect Diagram
Measurement
Variable
Machine
Material
Man
Measurement
Method
Environment
calibration of the digital scale
sweating hands
contents
position
tool correction
dust
humidity and temperature
isolating with gloves
door of equipment
well training
attitude
accuracy

## Slide 7: Data Collection
20 golf balls were randomly selected among 3 packs of golf balls.
Each golf ball was measured twice by each operator.
Operators wore gloves while measuring

## Slide 8: Row Data
Partial row data |  |  |  | 
Sample | Repeat | Operator1 | Operator2 | Operator3
1 | 1 | 45.7431 | 45.8102 | 45.7382
 | 2 | 45.7429 | 45.8101 | 45.7378
2 | 1 | 45.7619 | 45.7595 | 45.7557
 | 2 | 45.7617 | 45.7576 | 45.7551
3 | 1 | 45.6433 | 45.6388 | 45.6349
 | 2 | 45.6417 | 45.6366 | 45.6324
4 | 1 | 45.8269 | 45.8250 | 45.8224
 | 2 | 45.8263 | 45.8247 | 45.8212
5 | 1 | 45.7508 | 45.7470 | 45.7447
 | 2 | 45.7503 | 45.7460 | 45.7432
6 | 1 | 45.7510 | 45.7483 | 45.7434
 | 2 | 45.7505 | 45.7479 | 45.7431

## Slide 9: Data Analysis / Descriptive Statistic
Descriptive Statistic |  |  |  |  |  |  | 
Operator | N | Mean | St.Dev | Min | Max |  | P-value for Normality test*
1 | 40 | 45.7311 | .0775 | 45.5674 | 45.8561 | .00067 | .068
2 | 40 | 45.7315 | .0797 | 45.5643 | 45.8519 | .00085 | .042
3 | 40 | 45.7253 | .0776 | 45.5628 | 45.8492 | .00108 | .068
total | 120 | 45.7293 | .0777 | 45.5628 | 45.8561 | .00083 | 
*Shapiro-Wilk Normality Test |  |  |  |  |  |  | 
Descriptive Statistic |  |  |  |  |  |  | 
Operator | N | Mean | St.Dev | Min | Max |  | P-value for Normality test*
1 | 40 | 45.7311 | .0775 | 45.5674 | 45.8561 | .00067 | .068
2 | 40 | 45.7315 | .0797 | 45.5643 | 45.8519 | .00085 | .042
3 | 40 | 45.7253 | .0776 | 45.5628 | 45.8492 | .00108 | .068
total | 120 | 45.7293 | .0777 | 45.5628 | 45.8561 | .00083 | 
*Shapiro-Wilk Normality Test |  |  |  |  |  |  | 

## Slide 10: Data Analysis / ANOVA
ANOVA table |  |  |  |  | 
Source | DF | SS | MS | F | P
Operator | 2 | 0.000533 | 0.000267 | 0.92 | 0.405
Sample | 19 | 0.614033 | 0.032318 | 111.19 | <0.001*
Interaction | 38 | 0.013685 | 0.000360 | 1.24 | 0.225
Error | 60 | 0.017440 | 0.000291 |  | 
Total | 119 | 0.645691 |  |  | 
S = 0.01705 R2 = 97.30% R2-adj = 94.64% |  |  |  |  | 

## Slide 11: Data Analysis / Residual Analysis

## Slide 12: Data Analysis / Normality

## Slide 13: Process capability analysis
CP =
Cpu=
Sample Characteristics | 
 | 45.7293
s | .0777
USL | 45.93
CP | .79
CPu | .86
Sample Characteristics | 
 | 45.7293
s | .0777
USL | 45.93
CP | .79
CPu | .86

## Slide 14: Data Analysis / Gauge R&R Repeatability

## Slide 15: Data Analysis / Gauge R&R
Gauge Repeatability – Weight
P/T ratio = =0.05<10%
The gauge system is quite good.

## Slide 16: Conclusion
GRR is a good way to estimate the industry production process and capability.
Eliminate the errors of operators and Gauge.
ANOVA is the smallest bias
Classical GR&R and Long Form have same biases
If the numbers of measurements are very large there are no differences

## Slide 17: Thanks for your attention!