## Slide 1: Quality Management Final Report
Instructor: Prof. Jeh-Nan Pan
Group members:
Nguyen Thi Ngoc Hung (Sarah) – RA6017654
Nguyen Thu Thuy (Aki) - RA 8017058
Szu-Chen Ou – R26014103
Wan-Tzu Tsai – R26014064

## Slide 2: Outline
Part 1: Gauge R&R and Process Capability
Problem Formulation; Research Procedure and Methods
Data Collection and Analysis of Results
Part 2: Design of Experiment
Pareto Chart; Normal Probability Plot; Main Effect; Interaction Plot
ANOVA ; Regression Model; Predict Optimal Combination; Confirmation Test.
Conclusion

## Slide 3: Gauge R&R and Process Capability
Analysis for dry Primary Battery Size AA

## Slide 4: 1. Problem Formulation

## Slide 5: 1.1 Project Motivation
Batteries are very popular because of its portability, usefulness and availability for many applications in daily life.
However, not many researches have investigated the difference between batteries’ specifications produced by different brands.
To analyze whether some improvements in the production process are needed for manufacturers to maintain high quality standard by employing the Gauge R&R and Process Capability Analysis.
Process capability is ability of the process to realize a characteristic that will fulfill the requirements for that characteristic.
Several capability indices including Cp, Cpu, Cpl, and Cpk have been widely used in manufacturing industry to provide common quantitative measures on process potential and performance.

## Slide 6: 1.2 Product Introduction
Brands: Panasonic, Eveready, and Greencell
Panasonic: Neo Manganese Battery (1.5 voltage, AA size)
This is kind of dry cell battery, was made from Carbon zinc.
Panasonic Manganese Battery is ideal for devices that require a small and continuous supply of power such as clocks, remote controls and radio cassette recorder.

## Slide 7: 1.2 Product Introduction
Features:

## Slide 8: 1.2 Product Introduction
Eveready: Super Heavy Duty carbon-zinc battery (1.5 voltage, AA size)

## Slide 9: 1.2 Product Introduction
GreenCell: GP Greencell Extra Heavy Duty AA Battery.
The zinc chloride battery by GP Batteries is an improvement on the original zinc–carbon battery, using purer chemicals and giving a longer life and steadier voltage output as it is used.

## Slide 10: 1.2 Product Introduction

## Slide 11: 1.3 Research Purpose
To perform the measurements and minimize errors by studying the following factors:
The precision of the measurements: Expecting the potential errors which could be made by human errors and measuring instrument errors; developed detailed and cautious measuring procedure and employed measurement capability index to maintain the stability and capability of the measurement system
The variation of the product: Random samples from three brands; X bar and R charts are also applied.
Process capability: to examine whether the processes have met the product specifications.

## Slide 12: 1.4 Measurements Properties
To provide consistent measurement data is important in the control of any process for the same measurement objects and measurement system regardless of present or future should have the “stability”.
Measurement errors can only be diminished if the errors or variations contributed individually by each of these factors can also be minimized.
The same gage provide consistent measurement readings regardless of how many times the same operator of the gage repeats the measurement process.
The same gage can give consistent measurement readings no matter who performs the measurements under the same conditions

## Slide 13: 2. Research Procedure and Method

## Slide 14: 2.1 Measuring Process
Sampling Plan
Randomly Selected Samples
Cause Analysis Chart to define Control Variables
Assign Number to Products and Operators
Measure and Record the Length of the Samples
Calibrate the Caliber
Create random sampling order for measuring by operators, brands and samples
Identify samples by matrix paper
Measure and record the weights of the samples
Set up one calibrate the weight scale
Gauge R&R Analysis (GRR)
Process Capability Analysis (PCA)

## Slide 15: 2.2 Cause and Effect Diagram
5. Machines
Measurement Error
4. Material
1. Personnel
6. Environment
3. Measurements
2. Methods
Operating skills
Hands’ sweating
Measuring positions
Communication between operators and data key-in person
Variation between measuring and reading results
Defective products
Start from Zero
Caliper error
Weight scale error (not balanced…)
Temperature
Humidity
Vibration

## Slide 16: 3. Data Collection

## Slide 17: 3.1 Guidelines for the use of the instrument
1. Use the same measuring instruments.
2. After each measurement, calibrate the measuring tool.

## Slide 18: 3.2 Products and Instrument of Measurement
1. Products: Battery
2. Measuring Tools: Caliper and Precision Balances
Caliper
Precision Balances
Instrument Precision
Height: 0.01mm
Instrument Precision
Weight: 0.0001g

## Slide 19: 3.3 Measurement Parameter Determination
Number of battery: 20 pieces for each brand
Number of surveyor: 3
Frequency of measurement each surveyor: 2 times
Total Frequency of measurement: 3*2*20=120 times/brand

## Slide 20
4. Analysis of Results

## Slide 21: 4.1 Descriptive Statistics
Table 4.1.1 Descriptive statistics of height
Height | Panasonic | Eveready | Greencell
Mean | 50.217 | 49.851 | 49.875
StDev | 0.0964 | 0.110 | 0.0867
Minimum | 49.930 | 49.590 | 49.580
Q1 | 50.150 | 49.773 | 49.830
Median | 50.230 | 49.860 | 49.880
Q3 | 50.280 | 49.920 | 49.930
Maximum | 50.400 | 50.120 | 50.030
Range | 0.47 | 0.530 | 0.450
Table 4.1.2 Descriptive statistics of weight
Weight | Panasonic | Eveready | Greencell
Mean | 18.269 | 17.369 | 17.118
StDev | 0.0996 | 0.171 | 0.192
Minimum | 18.073 | 17.096 | 16.842
Q1 | 18.198 | 17.25 | 16.951
Median | 18.302 | 17.342 | 17.119
Q3 | 18.331 | 17.573 | 17.208
Maximum | 18.464 | 17.625 | 18.28
Range | 0.391 | 0.529 | 1.439

## Slide 22: 4.2 R Control Chart
Panasonic - Height
Figure 4.2.1 R chart of height (Panasonic)
Figure 4.2.2 R chart of height (Panasonic) after excluding outliers
Outliers
Out of control Process

## Slide 23: 4.2 R Control Chart
Panasonic - Weight
Figure 4.2.3 R chart of weight (Panasonic)
Figure 4.2.4 R chart of weight (Panasonic) after excluding outliers
Outliers
In control process

## Slide 24
4.2 R Control Chart
Eveready - Height
Figure 4.2.5 R chart of height (Eveready)
Figure 4.2.6 R chart of height (Eveready) after excluding outliers
Outliers
Out of control Process

## Slide 25
4.2 R Control Chart
Eveready - Weight
Figure 4.2.7 R chart of weight (Eveready)
Figure 4.2.8 R chart of weight (Eveready) after excluding outliers
Outliers
In control Process

## Slide 26
4.2 R Control Chart
Greencell - Height
Figure 4.2.9 R chart of height (Greencell)
Figure 4.2.10 R chart of height (Greencell) after excluding outliers
Outliers
In control Process

## Slide 27
4.2 R Control Chart
Greencell - Weight
Figure 4.2.11 R chart of weight (Greencell)
Figure 4.2.12 R chart of weight (Greencell) after excluding outliers
Outliers
In control Process

## Slide 28: 4.3 ANOVA and Residual Analysis
The purpose of the experiment is to check whether the different operators and brands will influence the results obtained.
Assume validity:
  1. The random errors are normally distributed.
  2. The random errors have constant variance .
  3. The random errors have zero mean.

## Slide 29: 4.3.1 ANOVA and Residual Analysis for Height
Table 4.3.1 Two-way ANOVA with interaction
Source | DF | SS | MS | F | P
Operator | 2 | 0.5004 | 0.25019 | 30.05 | 0.000
Brand | 2 | 10.0872 | 5.04361 | 605.84 | 0.000
Interaction | 4 | 0.0135 | 0.00339 | 0.41 | 0.804
Error | 351 | 2.9221 | 0.00833 |  | 
Total | 359 | 13.5232 |  |  | 
S = 0.09124 R-Sq = 78.39% R-Sq(adj) = 77.90% |  |  |  |  | 
Figure 4.3.2 Residual Plots for Height

## Slide 30: 4.3.2 ANOVA and Residual Analysis for Weight
Table 4.3.3 Two-way ANOVA with interaction
Figure 4.3.4 Residual Plots for Weight
Source | DF | SS | MS | F | P
Operator | 2 | 87.9660 | 43.9830 | 1716.90 | 0.000
Brand | 2 | 0.0059 | 0.0030 | 0.12 | 0.891
Interaction | 4 | 0.0108 | 0.0027 | 0.11 | 0.981
Error | 351 | 8.9918 | 0.0256 |  | 
Total | 359 | 96.9745 |  |  | 
S=0.1601 =90.73% (adj)=90.52% |  |  |  |  | 
Source | DF | SS | MS | F | P
Operator | 2 | 87.9660 | 43.9830 | 1716.90 | 0.000
Brand | 2 | 0.0059 | 0.0030 | 0.12 | 0.891
Interaction | 4 | 0.0108 | 0.0027 | 0.11 | 0.981
Error | 351 | 8.9918 | 0.0256 |  | 
Total | 359 | 96.9745 |  |  | 

## Slide 31: 4.4 Gauge R&R Analysis
Ratio | Gauge Indicators
1. P/T ratio | ≤ 10%: the gauge capability is adequate 10% < P/T ratio < 25%: the gauge capability is not adequate but acceptable ≥ 25%: the gauge capability is not acceptable
2. SNR (Signal and Noise) ratio | AIAG define it as the number of distinct categories that can be reliably obtained from measurements. SNR ≥ 5: the precision of gauge is adequate
3. DR (Discrimination) ratio | DR > 4: 𝑡ℎ𝑒 𝑔𝑎𝑢𝑔𝑒 𝑖𝑠 𝑐𝑎𝑝𝑎𝑏𝑙𝑒
Ratio | Gauge Indicators
1. P/T ratio | ≤ 10%: the gauge capability is adequate 10% < P/T ratio < 25%: the gauge capability is not adequate but acceptable ≥ 25%: the gauge capability is not acceptable
2. SNR (Signal and Noise) ratio | 
3. DR (Discrimination) ratio | DR > 4: 𝑡ℎ𝑒 𝑔𝑎𝑢𝑔𝑒 𝑖𝑠 𝑐𝑎𝑝𝑎𝑏𝑙𝑒

## Slide 32: 4.4.1 Gauge R&R Analysis for Height
Panasonic - Height
Figure 4.4.1 Gage R&R Study - ANOVA Method
Table 4.4.2 Gage R&R
Source | VarComp | %Contribution (of VarComp) | StdDev (SD) | Study Var (6 SD) | %Study Var (%SV)
Total Gage R&R | 0.003916 | 39.33 | 0.06257 | 0.37548 | 62.71
Repeatability | 0.001408 | 14.14 | 0.03752 | 0.22516 | 37.61
Reproducibility | 0.002507 | 25.19 | 0.05007 | 0.30047 | 50.19
Operator | 0.001223 | 12.29 | 0.03497 | 0.20985 | 35.05
Operator*Part | 0.001284 | 12.90 | 0.03584 | 0.21504 | 35.92
Part-To-Part | 0.006041 | 60.67 | 0.07772 | 0.46635 | 77.89
Total Variation | 0.009957 | 100.00 | 0.09978 | 0.59872 | 100.00
Number of Distinct Categories = 1 |  |  |  |  | 

## Slide 33: 4.4.1 Gauge R&R Analysis for Height
Panasonic - Height
P/T ratio and DR ratio shows the gauge capability is acceptable.
But SNR show the precision of gauge is inadequate.

## Slide 34: 4.4.1 Gauge R&R Analysis for Height
Eveready - Height
Figure 4.4.3 Gage R&R Study
Table 4.4.4 Gauge R&R
Source | VarComp | %Contribution (of VarComp) | StdDev (SD) | Study Var (6 * SD) | %Study Var (%SV)
Total Gage R&R | 0.00646 | 48.72 | 0.080408 | 0.48244 | 69.80
Repeatability | 0.00222 | 16.79 | 0.047205 | 0.28323 | 40.98
Reproducibility | 0.00423 | 31.93 | 0.065093 | 0.39055 | 56.51
Operator | 0.00276 | 20.86 | 0.052613 | 0.31568 | 45.67
Operator*Part | 0.00146 | 11.07 | 0.038327 | 0.22995 | 33.27
Part-To-Part | 0.00680 | 51.28 | 0.082490 | 0.49493 | 71.61
Total Variation | 0.01327 | 100.00 | 0.115195 | 0.69117 | 100.00
Number of Distinct Categories = 1 |  |  |  |  | 

## Slide 35: 4.4.1 Gauge R&R Analysis for Height
Eveready - Height
All indicators show the precision of gauge is inadequate.

## Slide 36: 4.4.1 Gauge R&R Analysis for Height
Greencell - Height
Figure 4.4.5 Gauge R&R Study
Table 4.4.6 Gauge R&R
Source | VarComp | %Contribution (of VarComp) | StdDev (SD) | Study Var (6 * SD) | %Study Var (%SV)
Total Gage R&R | 0.00424 | 50.52 | 0.065134 | 0.39080 | 71.08
Repeatability | 0.00154 | 18.34 | 0.039242 | 0.23545 | 42.82
Reproducibility | 0.00270 | 32.18 | 0.051985 | 0.31191 | 56.73
Operator | 0.00213 | 25.45 | 0.046230 | 0.27738 | 50.45
Operator*Part | 0.00056 | 6.73 | 0.023774 | 0.14264 | 25.94
Part-To-Part | 0.00415 | 49.48 | 0.064457 | 0.38674 | 70.34
Total Variation | 0.00839 | 100.00 | 0.091636 | 0.54982 | 100.00
Number of Distinct Categories = 1 |  |  |  |  | 

## Slide 37: 4.4.1 Gauge R&R Analysis for Height
Greencell - Height
All indicators show the precision of gauge is inadequate.

## Slide 38: 4.4.2 Gauge R&R Analysis for Weight
Panasonic - Weight
Figure 4.4.7 Gauge R&R Study
Table 4.4.8 Gauge R&R
Source | VarComp | %Contribution | StdDev(SD) | StudyVar (6*SD) | %Study Var(%SV)
Total Gage R&R | 0.0000002 | 0.00 | 0.00045 | 0.002738 | 0.45
Repeatability | 0.0000002 | 0.00 | 0.00045 | 0.002738 | 0.45
Reproducibility | 0 | 0 | 0 | 0 | 0
Operator_p | 0 | 0 | 0 | 0 | 0
Part –to-part | 0.0103586 | 100 | 0.10177 | 0.610664 | 100.00
Total variation | 0.0103588 | 100 | 0.10177 | 0.610670 | 100.00
Notes: From Figure 4.4.5, the main effect of measurement variability is the Part-to-Part.
The estimate of S/N ratio is larger than 5 and so is DR ratio. Both indicators show the precision
of gauge is excellent.

## Slide 39: 4.4.2 Gauge R&R Analysis for Weight
Eveready - Weight
Figure 4.4.9 Gauge R&R Study
Table 4.4.10 Gauge R&R
Source | VarComp | %Contribution | StdDev(SD) | StudyVar (6*SD) | %Study Var(%SV)
Total Gage R&R | 0.000010 | 0.04 | 0.003308 | 0.01985 | 1.90
Repeatability | 0.000010 | 0.04 | 0.003308 | 0.01985 | 1.90
Reproducibility | 0 | 0 | 0 | 0 | 0
Operator_e | 0 | 0 | 0 | 0 | 0
Part –to-part | 0.030344 | 99.96 | 0.174195 | 1.04517 | 99.98
Total variation | 0.030355 | 100.00 | 0.174227 | 1.04536 | 100.00
Notes: From Figure 4.4.9, the main effect of measurement variability is the Part-to-Part.
The estimate of S/N ratio is larger than 5 and so is DR ratio. Both indicators show the precision
of gauge is excellent.

## Slide 40: 4.4.2 Gauge R&R Analysis for Weight
Greencell - Weight
Figure 4.4.11 Gauge R&R Study
Table 4.4.12 Gauge R&R
Source | VarComp | %Contribution | StdDev(SD) | Study Var (6*SD) | %Study Var(%SV)
Total Gage R&R | 0.008323 | 21.94 | 0.091234 | 0.54740 | 46.84
Repeatability | 0.008322 | 21.93 | 0.091228 | 0.54737 | 46.83
Reproducibility | 0.000001 | 0 | 0.001071 | 0.00643 | 0.55
Operator_g | 0.000001 | 0 | 0.001071 | 0.00643 | 0.55
Part –to-part | 0.029619 | 78.06 | 0.172104 | 1.03262 | 88.35
Total variation | 0.037943 | 100.00 | 0.194791 | 1.16874 | 100.00
Notes: From Figure 4.4.11, the main effect of measurement variability is the Part-to-Part.
The estimate of S/N ratio is 2.66754 smaller than 5 and DR ratio is 4.558 larger than 4.

## Slide 41: 4.4.3 Conclusion
When measuring height, almost all indicators show the precision is inadequate no matter which brand is.
Different measuring angle, operator’s strength or other factors might give rise to large reproducibility.
For weight, the Gauge R&R performs well.

## Slide 42: 4.5 Process capability analysis
Let
USL=50.5 mm, LSL=49.2 mm and the target=49.85
to calculate the process capability
Figure 4.5.1 Round battery- Designation AA (protruding negative)
Source: American National Standards Institute Inc. (2001)

## Slide 43: 4.5 Process capability analysis
 | Panasonic | Eveready | Greencell
 | 4.7127324 | 3.1195075 | 3.8393939
 | 2.0496761 | 1.8285113 | 3.693496
 | 1.4248281 | 3.119457 | 3.7833708
 | 0.6196906 | 1.8284817 | 3.6396017
 | Panasonic | Eveready | Greencell
 | 4.7127324 | 3.1195075 | 3.8393939
 | 2.0496761 | 1.8285113 | 3.693496
 | 1.4248281 | 3.119457 | 3.7833708
 | 0.6196906 | 1.8284817 | 3.6396017
> 1
~

## Slide 44: Design of Experiment
fractional factorial design

## Slide 45: Purpose
We are interested in determining which process variables (factors) affect the launching distance.
Furthermore, we want to determine the region in the important factors that lead to the best possible response (Optimize).

## Slide 46: Process
Generate the fractional factorial design and run order.
Fix CAT-100 catapult.
Stick the scotch tape on the table.
Check the run order and the combination of factors to adjust catapult.
Put the ball on the ball seat position and eject.
Measure the eject distance.

## Slide 47: Analysis
Pareto Chart
Normal Probability Plot
Main Effect
Interaction Plot
ANOVA
Regression Model
Predict Optimal Combination
Confirmation Test

## Slide 48: 1. Pareto Chart
Under
All factors except AF are significant because these factors lie in the right of the red line.

## Slide 49: 2. Normal Probability Plot
All factors are all significant which is accordance with the result of Pareto chart

## Slide 50: 3. Main Effect
All main effects are significant, we check the main effect plot to see what the best combination is. The best combination is A(1) B(-1) C(-1) D(1) E(1) F(1)

## Slide 51: 4. Interaction Effect Plot
By the Interaction Plot, we can find that except AF interaction effect, the other 2-way interaction effects are significant.

## Slide 52: 5. ANOVA
Source | DF | Seq SS | Adj SS | Adj MS | F | P
Main Effects | 6 | 17113.8 | 17113.8 | 2852.30 | 184.93 | 0.000
Upright Arm Tension Location (A) | 1 | 3896.9 | 3896.9 | 3896.88 | 252.65 | 0.000
Projector Elevation (B) | 1 | 3525.4 | 3525.4 | 3525.39 | 228.57 | 0.000
Turn Table Position (C) | 1 | 2403.5 | 2403.5 | 2403.45 | 155.83 | 0.000
Pivot Arm Tension Location (D) | 1 | 4819.8 | 4819.8 | 4819.83 | 312.49 | 0.000
Ball Seat Position (E) | 1 | 2234.9 | 2234.9 | 2234.93 | 144.90 | 0.000
Ball Type (F) | 1 | 233.3 | 233.3 | 233.33 | 15.13 | 0.006
Residual Error | 9 | 138.8 | 138.8 | 15.42 |  | 
Lack of Fit | 1 | 4.7 | 4.7 | 4.73 | 0.28 | 0.610
Pure Error | 8 | 134.1 | 134.1 | 16.76 |  | 
Total | 15 | 17252.6 |  |  |  | 

## Slide 53: Assumptions
After ANOVA, we should check if the model follows 4 assumptions:
The residuals are normally distributed.
The residuals have constant variance .
The residuals have zero mean.
The residuals are independence

## Slide 54: Check Assumptions

## Slide 55: Check Assumptions

## Slide 56: Check Assumptions

## Slide 57: 6. Regression Model
Predictor | Coefficient | SE Coef | T | P
Constant | 111.356 | 1.023 | 108.80 | 0.000
Upright Arm Tension Location (A) | 15.6063 | 1.023 | 15.25 | 0.000
Projector Elevation (B) | -14.8438 | 1.023 | -14.50 | 0.000
Turn Table Position (C) | -12.2563 | 1.023 | -11.97 | 0.000
Pivot Arm Tension Location (D) | 17.3562 | 1.023 | 16.96 | 0.000
Ball Seat Position (E) | 11.8188 | 1.023 | 11.55 | 0.000
Ball Type (F) | 3.8187 | 1.023 | 3.73 | 0.006
Upright Arm Tension Location*Ball Type (AF) | 0.544 | 1.023 | 0.53 | 0.610
S = 4.09397 R-Sq = 99.2% R-Sq(adj) = 98.5% |  |  |  | 

## Slide 58: 6. Regression Model
Predictor | Coefficient | SE Coef | T | P
Constant | 111.356 | 0.982 | 113.42 | 0.000
Upright Arm Tension Location (A) | 15.6063 | 0.9818 | 15.90 | 0.000
Projector Elevation (B) | -14.8438 | 0.9818 | -15.12 | 0.000
Turn Table Position (C) | -12.2563 | 0.9818 | -12.48 | 0.000
Pivot Arm Tension Location (D) | 17.3562 | 0.9818 | 17.68 | 0.000
Ball Seat Position (E) | 11.8188 | 0.9818 | 12.04 | 0.000
Ball Type (F) | 3.8187 | 0.9818 | 3.89 | 0.004
S = 3.92733 R-Sq = 99.2% R-Sq(adj) = 98.7% |  |  |  | 
After excluding AF interaction term.

## Slide 59: 7.Predict Optimal Combination
ANOVA prediction model:
By the ANOVA model, we can predict the optimal response is:
111.356+15.61+14.84+12.26+17.36+11.82+3.82=187.066

## Slide 60: 7.Predict Optimal Combination
Regression prediction model：
By the regression model, we can predict the optimal response is:
111.356+15.6063+14.8438+12.2563+17.3562+1
1.8188+3.8187=187.0561

## Slide 61: 8. Confirmation Test
Prediction Error |  |  | 
No | Observations | Regression model error | ANOVA model error
3 | 132.3 | 2.64% | 2.305%
6 | 96 | 4.22% | 4.79%
9 | 132.6 | 0.193% | 0.603%
12 | 157.8 | 1.24% | 1.584%
15 | 152.8 | 1.99% | 1.636%
 |  | MAPE=2.0566% | MAPE=2.1836%
All prediction errors are smaller than 15% and MAPE smaller than 10%.
We can say both models have the ability to prediction.

## Slide 62: Conclusion
Use fractional factorial design (Resolution III).
The main effect may not be significant but due to the influential interaction effect cause the wrong conclusion.
We suggest that using or fractional factorial design would be better.

## Slide 63: Reference
Montgemery, D. C. (2005). Introduction to Statistical Quality Control. Jefferson City, US: John Wiley & Sons, Inc.
American National Standards Institute Inc. (2001). For Portable Primary Cells and Batteries With Aqueous Electrolyte - General and Specifications. U.S.
江巧玉，「量測系統重複性與再現性的分析研究」。
Chiang, C.-Y. (2002). A study of Gauge repeatability and reproducibility for measurement systems. (Master), National Cheng Kung University, Tainan, Taiwan.

## Slide 64: Thanks for Your Attention!