## Slide 1: To see a w rld in a nut
Quality Management
Group 2
R26994086 洪世庭
R26994094 簡婉茹
R26991101 黃山耘

## Slide 2: 1-1 Paper Industry Background in Taiwan
Domestic nut industry become a complete system of export-oriented production and marketing of metal products industry
Domestic nut industries covered a wide range of other industries.
In 2007, the proportion of nuts imports to a minimum, about 3.2%,and nut exports hit a new high.
Nut Industry
Development of peripheral industries mature
Automated production efficiency
Stable supply of raw materials

## Slide 3: 1-2Background
The machinery industry has become an integral part of daily life.
Because of industrial machinery should be precision, and the nut is the necessary parts, so the precision of the nut will usually affect the quality of mechanical.

## Slide 4: 1-2 Research Purpose
The screws is fixed by nuts, when the inner diameter of the nut is inconsistent or when there is a gap, will cause the screw cannot be fixed.
When the weight of the nut is inconsistent, the error may be caused by the proportion of components, it will cause insufficient strength.
Different inner diameter
Screws is fixed by nuts

## Slide 5: 2.Research Method
Quality control relies on a lot of measurements data analysis. In this study, to be discussed is the variability will result from the measurement system.
Usually want to measurements data should have accuracy and precision. In this study we focus on accuracy.
Accuracy
Gauge error
Operator Error
Analysis Methods
Classical GR&R: used concept about range from x-bar –R chart to estimate variance.
P/T ratio: used to assess whether this measure can accurately measure the quality characteristics of products.
ANOVA analysis: We want to understand the variation between factors, also estimate reproducibility and repeatability.

## Slide 6: 3.The procesure of data collection
Samples: thirty nuts
Measuring instrument : Vernier Caliper、Electronic scale
The steps are as following:
(1)Number these thirty nuts
(2)Using minitab to randomize measuring order
(3)Using the same method to measure the weight of nuts
(4)Each operators measure twice.
(4)Recording the value
(5)Complete the measuring work

## Slide 7: 4.Data Analysis Descriptive statistics of Inner Diameter of Nuts
Operators | N | Mean | StDev | Min | Max
Qwoop | 60 | 9.4340 | 0.0214 | 9.3800 | 9.4900
Wendy | 60 | 9.4220 | 0.0196 | 9.3700 | 9.4700
Tony | 60 | 9.4307 | 0.0187 | 9.3900 | 9.4700
Total | Mean | StDev | Operators | Parts | Replication
180 | 9.4289 | 0.0204 | 3 | 30 | 2
We have the upper and lower bond of inner diameter of nuts by table 4.1 and
The upper and lower bond of inner diameter of nuts is
(9.3473 , 9.5105)

## Slide 8: 4.Data Analysis Normal probability plot of Inner Diameter of Nuts
Anderson-darling Test
Ho: Data from normal distribution
Ha: Data do not from normal
distribution
All the P-value are smaller than 0.05, therefore, it is significant that the data (inner diameter of nuts) do not from normal distribution.

## Slide 9: 4.Data Analysis R - chart for inner diameter of nuts
Figures show that the R-chart in control indicating all the samples lie between control limits.

## Slide 10: 4.Data Analysis Gauge Repeatability and Reproducibility for inner diameter of nuts
Source | VarComp | %Contribution | StdDev (SD) | (6 * SD) | (%SV)
Total Gage R&R | 0.0002899 | 56.00 | 0.0170255 | 0.102153 | 74.83
Repeatability | 0.0002546 | 49.19 | 0.0159574 | 0.095745 | 70.14
Reproducibility | 0.0000352 | 6.81 | 0.0059354 | 0.035612 | 26.09
Part-To-Part | 0.0002278 | 44.00 | 0.0150922 | 0.090553 | 66.33
Total Variation | 0.0005176 | 100.00 | 0.0227518 | 0.136511 | 100.00
Number of Distinct Categories = 8 |  |  |  |  | 
Because we do not have the USL and LSL of inner diameter of nuts, so we assume
to get the upper and lower bond is (9.3473 , 9.5105).
And P/T ratio is
Xbar-R Method

## Slide 11: 4.Data Analysis Gauge Repeatability and Reproducibility for inner diameter of nuts

## Slide 12: 4.Data Analysis Gauge Repeatability and Reproducibility for inner diameter of nuts
Source | DF | SS | MS | F | P
Part | 29 | 0.0282111 | 0.0009728 | 2.82645 | 0.000
Operator | 2 | 0.0046044 | 0.0023022 | 6.68908 | 0.002
Part*Operator | 58 | 0.0199622 | 0.0003442 | 1.40799 | 0.072
Repeatability | 90 | 0.0220000 | 0.0002444 |  | 
Total | 179 | 0.0747778 |  |  | 
The P/T ratio was once again computed:
ANOVA Method

## Slide 13: 4.Data Analysis Descriptive statistics of Nuts’ weight
We have the upper and lower bond of weight of nuts by table 4.1 and
Operators | N | Mean | StDev | Min | Max
Qwoop | 60 | 10.208 | 0.133 | 10.062 | 10.682
Wendy | 60 | 10.208 | 0.133 | 10.061 | 10.682
Tony | 60 | 10.208 | 0.133 | 10.062 | 10.682
Total | Mean | StDev | Operators | Parts | Replication
180 | 10.208 | 0.132 | 3 | 30 | 2
The upper and lower bond of nuts’ weight is
(9.68 , 10.736)

## Slide 14: 4.Data Analysis Normal probability plot of Weight of Nuts
Anderson-darling Test
Ho: Data from normal distribution
Ha: Data do not from normal
distribution
All the P-value are smaller than 0.05, therefore, it is significant that the data (weight of nuts) do not from normal distribution.

## Slide 15: 4.Data Analysis R - chart for Weight of Nuts
Figures show that the R-chart in control indicating all the samples lie between control limits.

## Slide 16: 4.Data Analysis Gauge Repeatability and Reproducibility for Weight of Nuts
Source | VarComp | %Contribution | StdDev (SD) | (6 * SD) | (%SV)
Total Gage R&R | 0.0000001 | 0.00 | 0.000281 | 0.001684 | 0.19
Repeatability | 0.0000001 | 0.00 | 0.000266 | 0.001596 | 0.18
Reproducibility | 0.0000000 | 0.00 | 0.000090 | 0.000538 | 0.06
Part-To-Part | 0.0230119 | 100.00 | 0.151697 | 0.910181 | 100.00
Total Variation | 0.0230120 | 100.00 | 0.151697 | 0.910183 | 100.00
Number of Distinct Categories = 762 |  |  |  |  | 
Because we do not have the USL and LSL of inner diameter of nuts, so we assume
to get the upper and lower bond is (9.68 , 10.736).
And P/T ratio is
Xbar-R Method

## Slide 17: 4.Data Analysis Gauge Repeatability and Reproducibility for Weight of Nuts

## Slide 18: 4.Data Analysis Gauge Repeatability and Reproducibility for Weight of Nuts
Source | DF | SS | MS | F | P
Part | 29 | 3.133275 | 0.108044 | 403715 | 0.000
Operator | 2 | 0.000001 | 0.000001 | 2 | 0.127
Part*Operator | 58 | 0.000016 | 0.000000 | 1 | 0.053
Repeatability | 90 | 0.000017 | 0.000000 |  | 
Total | 179 | 179 | 3.133308 |  | 
The P/T ratio was once again computed:
ANOVA Method

## Slide 19: 5.Conclusion
(1)In the experiment,the P/T ratio of inner diameter of nuts are larger than 0.1,which indicates that the caliper we used to experiment or operators themself cause large variation.
(2)The P/T ratio of weight of nuts are very
small.

## Slide 20: 6.Suggestion
(1) If we still want to measure the inner diameter of nuts,the most important thing is to stipulate the measuring rules.Something like we can put the nuts on the desk rather than take it in the hand.
(2)We can choose the measuring items which is a
plane to make it measured more easily.

## Slide 21
Thanks for your attention